## Slide 1: 5 Litre Rack
April 2016

## Slide 2
2 x strong poles
of about 40mm D
and 2500mm length
4 x 1200mm cross beams of about 25mm D
A third pole if you
want the rack to
be free standing
There is no need for the third pole if the rack is leaning against a wall

## Slide 3
300mm of strong
single-core cable
Drill 4mm holes at 2400mm
on the two uprights and at
2500 on the support beam.

## Slide 4
Put marks on the uprights
at 380mm from the bottom

## Slide 5
…and 760mm

## Slide 6
… and 1140

## Slide 7
… and at 1520

## Slide 8
Tie the top ends of the
uprights together

## Slide 9
Then tie on the support pole

## Slide 10
8 x 3mm strong cord
burnt and knotted at
both ends
340mm long

## Slide 11
8 x retaining wires
(150mm)
8 x toggles

## Slide 13
Set out the poles in an
“A” shape with the legs
of the “A” as wide as
possible. Place the cross
beams under the uprights

## Slide 14
Tie the cord around the upright and the cross beam with a loose double reef knot.

## Slide 15
Insert the toggle and twist. This will cause the cross beam to be lifted upwards a bit which is what you want. Secure the end of the toggle with the retaining wire.
Repeat for the right side bringing the cross beam back parallel.

## Slide 20
Punch a marker hole
for an irrigation point
(optional)

## Slide 22
Punch marker holes x 5
at the lowest point

## Slide 23
Drill drainage holes
(8mm)