## Slide 1: Soil Moisture Sensor Project Two Presentation Two
Colin McAllister & Daeyoo Kim

## Slide 2: Project Review
Building wireless soil moisture probe
Controlled by esp32 microcontroller
Powered by single-cell lithium ion battery and solar panel
External temperature compensated RTC manages ESP32’s sleep mode and ensures consistent measurements
Obtains soil moisture by measuring dielectric permittivity of soil with capacitive probe

## Slide 3: Probe Schematic
Three core elements to circuit
ESP32
Power management
Real-time clock
Connectors
Programmer board
Solar cell
Battery
Battery thermistor

## Slide 4: Power management
MCP73871
Manages single cell lithium battery
Temperature dependent charging using 10kΩ thermistor
Prioritizes load over battery when input voltage is applied
LM3724
Open drain output pin disables ESP32 when lithium cell drops below 2.5v
TPS63021
Buck-boost converter to regulate battery output to 3.3 volts

## Slide 5: Programmer board
Wanted a detachable way to program the soil probe
Small board converts USB to Serial
Uses CP2102N USB Bridge
Common design used with most ESP32 breakout boards
Features two BJT transistors that toggle EN and IO0 pins on ESP32 to trigger device to enter bootloader mode
CP2102N independently powered by own 5 volt to 3.3 volt fixed linear regulator
Interfaces with soil probe using 8-pin header

## Slide 6: Prototyping
Tested integrating the RTC with the ESP32
Communicates over I2C bus
Programming current time
Setting alarm interrupt and using alarm to wake from deep sleep
Tested capacitive touch pin with measuring soil moisture
Saw slight change in capacitor sensor’s output voltage when placed in different soil moistures

## Slide 7: Power testing
Current Consumption at 3.3 volts
  In deep sleep: 2.436 mA
  Active: 43.3 mA
Assuming 1 measurement per hour
Time to conduct and transmit measurement (seconds) | Estimated daily current consumption (mAh)
1 | 58.74
5 | 59.83
10 | 61.19
15 | 62.55
30 | 66.64
45 | 70.72
60 | 74.81
120 | 91.16

## Slide 8: Battery selection
Want to select a battery that will last about a week without solar power
Battery Size (mAh) | Minimum Lifetime (days) | Maximum Lifetime (days)
350 | 3.8 | 6.0
400 | 4.4 | 6.8
500 | 5.5 | 8.5
1200 | 13.2 | 20.4
2000 | 21.9 | 34.1

## Slide 9: Moisture sensor board layout
Board size:
1.4” x 3.7”

## Slide 10: Programmer board layout
Board size:
0.8” x 0.87”

## Slide 11: Software
Code written in C and compiled with Espressif’s ESP-IDF SDK
Structure: one main file plus two libraries
  Main file
    Measures soil, establishes wireless connection, and uploads to static IP over TLS/SSL
  Nonvolatile memory helper library
    Stores and retrieves variables saved in nonvolatile memory
  RTC helper library
    Configures and reads/writes to RTC over I2C
Code available on Github
  https://github.com/colin-pm/soil_moisture_meter

## Slide 12: Questions?