## Slide 1: Towards More Agile and Inexpensive Robotics
Darren Levine

## Slide 2: Current Progress In Agile Robotics
Motivations:
  Medical care, Emergency scenarios, Advancements in prosthetics/transhumanism
  Advances in manufacturing, liberation from menial/dangerous labor
  Already many specialized robotics systems, 3D printers, Roombas, etc.
  Emerging fields: Soft robotics, Foldable Robotics
Why Focus on Agility?
  Common capability needed for human like generalization / fluid action
    Systems have a hard time generalizing, a system built for one task will not perform at another
  Interacting in a world built for the human form
   Humanoid Robotics, Legged Robotics
   Moving towards/past “Human Like” Capabilities
Why Focus on Cost?
  Low Proliferation: Specialization and niche markets
  Slow development, limited access to software/hardware
State of the art in agile humanoid robotics ( >> $1M)
  Boston Dynamics Atlas, & Handle
  Honda Asimo & E2-DR, Nasa Valkyrie, Toyota T-HR3
  DRC-Hubo won the 2015 DARPA challenge
  Still a high degree of Teleoperation / Scripted Action
Why is this problem difficult, and what are potential solutions?
Cost
Execution Time Compared to a Human for Non-Specialized Tasks
Atlas 2017 (2/3 of human time)
0 0.3 0.6 1/1 1.3
Superhuman
DARPA Neurally Controlled Prosthetic

## Slide 3: Before we discuss the problem…
Boston Dynamics: Atlas-11/16/2017

## Slide 4: Breaking Down Tasks in Robotics
Develop High Level Motivation
  Clean a Room, Fly a Mission Route, etc.
Represent the problem / Learn
  Knowledge representation framework
Generate a Goal/Dependency Tree
  Search and optimization for relevant dependencies
Step Through each Action
  Utilize a Control System, example: Visual Servoing
Each of step requires multiple interfaces with environment, errors propagate
Software
Robot
World
Physical Contact
Computer Vision
Lidar, Other Sensors…
Hardware Modeling
Environmental Modeling
Planning
What actually happens
What we want to happen
Generalizable
Typically done by a human
Highly Specific, Sometimes Scripted
Knowledge of Reasoning, Cause and Effect
Has knowledge or an ability to obtain knowledge
Inherently Unstable, Expensive, Multidisciplinary Problem, Cascading Levels of Complexity!

## Slide 5: Example: Classical Deductive Chain Approach
Develop High Level Motivation
  Clean a Room, Fly a Mission Route, etc.
Represent the problem / Learn
  Knowledge representation framework
Generate a Goal/Dependency Tree
  Search and optimization for relevant dependencies
Step Through each Modularized Action:
Self Localization
SLAM/Computer Vision
Put X in Y
X=trash, Y=bin
What a X/Y looks like, how to navigate through Z, What the action “Put” means with X in relation to Y
1) Locate Y in Z
2) Navigate to Y
3) “Put” X in Y
Recognize Bin
Computer Vision
Locate Bin
Relative to Self
Computer Vision/
Geolocation Math
Visually Servo to XYZ Position Above Bin
Encoders/INS
Release Trash Above Bin
Control System, model of how trash will fall
This works (sometimes)! And the flow of deduction is easy to understand.
Apparent problems with this approach:
Not executed as a fluid action.
Often much slower than a human, each step is elaborate and needs dedicated processing time.
Compounding errors often need error loop closure to route through a long action chain.
Hand designed and requires a lot of processing power
Emergent Behavior is hard to come by (behavior is not easily generalizable to other tasks)
Compounding Errors

## Slide 6: Do humans approach tasks this way?
Sergey Levine’s thought experiment to assess modern robotics:
  Given two simple tasks:
  Open a door and walk through it
  Open a door and walk through it while blindfolded
  Result: A human completes the task ~7x faster (even when blindfolded) than a 2015 DARPA challenge humanoid robot.

## Slide 7: Do humans approach tasks this way?
Sergey Levine’s thought experiment to assess modern robotics:
  Given two simple tasks:
  Open a door and walk through it
  Open a door and walk through it while blindfolded
  Result: A human completes the task ~7x faster (even when blindfolded) than a 2015 DARPA challenge humanoid robot.
The robots often fail when not in a controlled environment

## Slide 8: Hypothesis as to why the robot is slow
Sensory: If the robot had force feedback, vision, it’d do the task just as well
  Emerging robots often do have these senses
  Note: The human still completed the task while blindfolded
Hardware: The robot simply can’t move as fast, a hardware limitation
  Often they can move faster. (Though latency/ real-time control can be an issue)
Software/Processing: Better software (planning algorithms, computer vision, etc.) would enable superhuman speeds
  Seems likely.
    So how do we get there?
    And is the classic modular deductive chain approach the best way? Or does changing how information flows through the task pipeline provide a benefit.
Asking the robot designer why:
  Safety: A slower robot helps keep the robot & handler safe (even humans make mistakes, but we aren’t 500lb pieces of metal)
  Complexity: All that sensory information and planning needs time to process and is subject to many forms of compounding error
Improve software.
Potential Answer: By reducing a “Certain Type of Complexity”

## Slide 9: Biological Inspiration: What type of “Complexities” does the mind reduce?
Benjamin Libet’s pioneering experiments with humans:
  An athlete would precisely hit a ball before being aware of that decision
    Found that conscious awareness lags 200-300 milliseconds behind subconscious awareness
  There’s no time for chains of reasoning/deduction when it comes to agile movements
Human’s must rely on extremely fast subconscious motor routines or these amazing feats wouldn’t be possible
  Idea: Maybe this mechanism can be extend into the non-agile long-term task planning realm…
How are fast subconscious actions possible when the problems are so complex?

## Slide 10: Biological Inspiration: How complex are these problems?
When we catch a ball we’re actually solving a complex set of differential equations
  Wind speed, air density, mass, size, drag…
How do you catch a ball?
  It’s tempting to answer with a highly-intelligent chain of reasoning
It turns out we use the “Gaze Heuristic” (Discovered by Gerd Gigerenzer):
  If ignore the fact they were solving complex problem and focus on one heuristic variable we can consistently solve the problem
  If the ball lowers in the sky: Run Faster
  If the ball raises in the sky: Run Slower
A case for the deductive tree approach:
There’s a dream that a robot could not just complete the action like a human, but could compute the optimal action at superhuman speeds.
Approach requires complex algorithms, faster sensors/processors = Costly
The problem your brain solves for agile tasks:
  Find simple representations of a complex problem dynamically as those problems change
  The “type of complexity” that is reduced is the representation of the problem at hand, simplifying the way information flows through your controller
  = Fast / Cheap Control
For slower tasks, we might merge methods

## Slide 11: Simple Controller “Stay Upright”
Ingredients:
1) System coordinate/force transformation
2) Foot_Velocity = 3 x Center_of_Mass_Velocity
Heuristics seem to work but Is a handmade control system / representation the best approach?
Program a car to drive itself1 on freeways = 1 month
  Experience diminishing returns when trying to make it drive like a human
1 https://medium.com/the-mission/how-to-build-a-self-driving-car-in-one-month-d52df48f5b07

## Slide 12: “Where” to search for Simple Representations? Terminology:
Reduced Dimensional Representation (Example: Cartesian  Joint Space )
  The human body has 244 degrees of freedom, controlled by 630 muscles
    Wouldn’t want to design a system that consciously controlled 630 actuators
  One type of dimensional representation may be more useful than another
    Avoiding the “curse of dimensionality” arising in high-dimensional spaces
Latent Space Representation
  Mathematical abstraction, not necessarily a directly observed variable
x
y
Controller Design Implications:
Inputs: Cartesian
Calculations: Continuous Latent space?
Output: Torques in Joint Space

## Slide 13: What does this transformed space look like?
Latent Space Representation for Punching/Fighting
(a) “Continuous Character Control with Low-Dimensional Embeddings”, Levine,S. et al.
Examples of System Transformations:
In rigid dynamics: Flow Fields
Infinite set mathematics:
  Hilbert curves - mapping of 2d space into 1d space
Exponential mapping:
  Fourier transform, taking a complicated looking system and splitting it up into a few relatively simple parts that completely describe the system
This can be designed by hand…

## Slide 14: Reduced Dimensional, Latent Space Representations
The goal is to Automatically Describe a Complex Problem so that:
  Lower computational load / Error contributions  Reducing the pipeline of information
  Make control easy  Transform a non-linear space into continuous linear space
  Easily generalizable  compact them into smooth representations, better than modules
Why does this work?
  Insights from AI: Intuitive understanding of physics often means an understanding that objects follow smooth paths, moves the system closer to a “intuition” of physicality
  Similar Successes: Extended Kalman Filter (pretends at linearity, instead of transforming into linearity)
How does this work? Optimize/Search given examples of desired movement:
    Covariance Matrix Adaptation Evolution Strategy (CMA)
    Gaussian Process Latent Variable Modeling (GPLVM)
    Nearly the entire field of Bayesian statistics…
  Deep Learning Neural Networks
Problems with method ( Black Box? ):
  Is this system Deterministic or “Optimal”? Must we sacrifice performance for certainty?
  The human brain still makes mistakes when it comes to intuition  Optical illusions
  How do we get around this in order to make the robot’s deterministic/dependable/safe in a way that human brains are not? Dependent on Method.
  Asimov’s 3 laws via Adversarial Networks
Slow Search Process! But smoothly generalizable.
Future: One Shot Learning

## Slide 15: Works That use Representational/Heuristic Methods
1983 MIT's Leg Lab
Custom designed Heuristic Controllers
2013 S. Levine, J. M. Wang
Learned Reduced Dimensional Latent Space Controllers
Still most capable / fastest dynamic balancing methods

## Slide 16: Software Conclusion
What’s needed Now:
  Open source libraries for learning low-dimensional latent space controllers from example or exploration
    The problem being solved by the controller is a lower dimensional/simpler one
    Cheaper computational hardware requirements
    Fewer sensors needed, less demanding sensor requirements
    Smoothly generalizable form, faster and more fluid
    Lowered development time cost
Future Research:
  Deep learning one-shot methods are a promising avenues to develop fast “muscle memory” like intuitions
  Extending this approach to large time scale tasks
Far Future:
  Merging with deductive knowledge based systems
  Asimov’s Three Laws via Adversarial Networks?
  Extend approach to transform system into a compact Riccatti time-variant form for deterministic optimal control

## Slide 17: Hardware
Video Game’s Popularity lead towards huge advancements in GPUs
Quadcopter’s popularity lead towards cheaper brushless motors, integrated/miniaturized flight controllers
The same needs to be done for Torque/Force Controlled systems:
  Control Techniques:
    Active Impedance, Stiffness
    Torque Control vs. Velocity Control
  Efficiency:
    Hardware optimization: Regenerative Breaking
    Software optimization: Towards Optimal Control for the System
  Actuator Choice:
    Hydraulics
    Custom high torque brushless gimbal motors
    Artificial Muscles
  Fast Direct Drive vs. Semi-Direct Drive vs. Fast update rate torque sensors in geared systems
Low Hanging Fruit:
  Actuator cost reduction and capability increase (piggyback off of quadcopters, but add IC torque control)
  Miniaturized Systems for research/development
  (smaller  cheaper)
  Software Advancements (open source libraries)
Cassie (Agility Robotics) Custom brushless motors
HEBI Robotics Actuator
ANYdrive Actuator

## Slide 18: Any Questions?
2017 Ghost Minitaur: Ghost Robotics
2017 BIP 1: Darren Levine