BusIO Commands / Responses

BusIO message is two byte message (16 bits) using standard RS232 little-endian format. The first byte is called BusByteL, second is BusByteH. Transmission speed 1200 bps.

The BusByteL usually contains data or dontcare. The BusByteH high’s nibble is always a command.

There are up to 16 possible command slots available. There are 16 unique device addresses available.

| ID | Low byte | High byte | Function |
| --- | --- | --- | --- |
| 0 | XX | 0X | Disarm / LED flash off (broadcast) |
| F | XX | FX | Arm / LED flash on (broadcast) |
| A | SS | Adev | Program trigger sensitivity value SS to device dev |
| B | XX | Bdev | Read sensor current value from device dev |
| C | Cdevnew | Cdev | Re-assign address of device dev to devnew |
| D | dD | Ddev | xxdd xDDD dd = NFB divideby DDD = NFB delay (samples) |
| E | II | Edev | (Readonly) II = integrator (trim) value |
| 5 | DD | 5dev | Alarm trigger from device dev , with data DD |
| 9 | (Flags) | 99 | Control options of GPRS Station ??? |
|  | 00 | 01 | Exit delay state |

X = don’t care      DEV = BusIO device address

Example commands:

Send    $00$F0       broadcast “Arm” command (+ LED flash)

Send    $00$B3       to read values from device 3:  trig. Thresh, NFB, intregator level

Send    $14$A3       program trigger thresh 14 to device 3

Send    $C4$C2      change device 2 address to 4

## At the BusIO physical layer

All devices are connected across a three-wire multidrop bus. 4 V , ground, and bi-directional serial bus 1200 bps.

The LSB of BusByteL sent first, the MSB of BusByteH is sent last

last                               first

|    <       <        <       <    |

76543210 	76543210

4 examples:

1010AAAA   DDDDDDDD     program address / 8 bit data

0101AAAA   DDDDDDDD     alarm / address  / data

0000xxxx   xxxxxxxx     LED flash off

1111xxxx   xxxxxxxx     LED flash Active on

Using BusIO to program sensors

Sending $00$B2  typical response from sensor 02:

BusIO sending data |

BusIO response data ^

00B220A2

04D2

28E2

# Text boxes

20 thresh

04

lownibble NFB divideby  hinibble NFB delay (samples)

28 integrator trim value