## Slide 1: Lil’ Buddy 2N3904/2N3906 Power Amplifier
John Guy

## Slide 2: INTRODUCTION
I had seen recent efforts to use parallel 2N3904 and 2N3906 transistors to make a power amplifier. This is my take on this exercise.

## Slide 3: PREAMPLIFIER
Modeled after NJM2068, but with NPN inputs
Q8 and Q9 run at 500µA
Q1-Q4 are a cross coupled quad for lower noise and resistance to thermal gradient
Recent addition is a second Baker clamp to improve clipping performance

## Slide 4: BIAS
A 5.6V Zener with a nominal 0mV/°C tempco has a diode in series to give it -2mV/°C tempco
This matches the tempco of VBE of Q34, thus stable bias over temperature
Q37 runs at 1mA
The preamp section runs at 500µA per leg
The output section has ±1mA and ±4mA bias inputs.

## Slide 5: OUTPUT
A complementary Darlington emitter follower input stage is followed by a complementary emitter follower output stage.
R15, 200Ω as shown, will be hand trimmed from 150Ω to 250Ω to establish bias on the ±12V supplies at 35mA with no load and input grounded.
Output current limit is ±11A, or about 700mA per transistor
At 3.7WRMS output power the peak power in each output transistor is 278mW, with an average power of 113mW

## Slide 6: thd
Vin = 1.4VPP at 1kHz
POUT = 3.7WRMS into 4Ω

## Slide 7: BANDWIDTH
Vin = 0.707RMS
POUT = 3.7WRMS into 8Ω
BW = 2.3MHz

## Slide 8: Current Limit
Current limit is about ±11A, suitable for 1Ω load at ±12V single ended, or 2Ω BTL.

## Slide 9: PCB TOP
85x40.5mm
3 mounting holes
This surface will be attached to heat sink via compliant thermal interface material
100% SMT components
All components have BOM designator, decoded on other sideof PCB

## Slide 10: PCB BOTTOM
85x40.5mm
3 mounting holes
This surface will be face up when PCB is attached to heatsink
6 through hole components on this side
BIAS potentiometer is adjusted for 35mA supply current at no load
OFFSET potentiometer is adjusted for 0VDC offset with no load, no input.

## Slide 11: THANK YOU