## Slide 1: Design of a Smart Step Counting System
Zachary Murtishi, University of Rhode Island

## Slide 2: Part I: Step counting

## Slide 3: What is a pedometer?
A pedometer is a device intended to count the number of steps performed by the wearer.
Pedometers can be a standalone device, or integrated into other devices such as smartphones, smart watches, health trackers, or even hearing aids. They may be implemented with mechanical counters or MEMS sensors and algorithms, though they are most commonly implemented with electronic circuits today.

## Slide 4: Current approaches to step counting
Pedometers of the past were often mechanical devices, though virtually all commercially-available pedometers today are electronic
Traditional algorithms used for step counting on many commercially-available pedometers
  Algorithms use data sourced from a MEMS accelerometer, gyroscope, or combination (IMU)
  Algorithms can be be simple or they can be highly-optimized
Academic studies have experimented with the use of neural networks and machine learning techniques for step counting
  Several examples, but these experiments are often not deployed for use in real time
  Very little use in commercial products
    Starkey Livio AI hearing aids claims to use AI, but no other information available

## Slide 5: Examples of step counting algorithms
Zero crossing detection
Windowed peak detection
Autocorrelation

## Slide 6: Part II: A smart step counting algorithm

## Slide 7: Using a neural network for step counting

## Slide 8: Artificial neural networks

## Slide 9: Two-step algorithm to count steps
Step 1: Motion classification
  Using a one-second window of IMU data sampled at 10 Hz, perform motion classification to determine if the user is in motion.
Step 2: Zero crossing algorithm
  If the motion classifier detects user motion, a zero crossing algorithm is run to determine the number of steps counted in the one-second window.
  The zero crossing algorithm simply counts the number of zero crossings observed in the gyroscope’s Z axis data to determine the number of steps that occurred in that window.
  Number of zero crossings = number of steps

## Slide 10: Motion classifier
The motion classifier is a model trained to identify a user’s current motion type
  Trained to detect idle behavior, active walking motion, and erratic motion (shaking)
  Model was trained using real-world data collected with a user-worn gyroscope
Implemented using Keras in Python
Motion classifier uses separate neural networks for each gyroscope axis
  Uses Y and Z axis of gyroscope to determine motion type
  Softmax outputs of each neural network
Takes a 10-element timeseries vector as input
  10 elements are sampled

## Slide 11: Part III: Implementations of a smart step counting system

## Slide 12: Hardware to implement a smart step counting system
A step counting algorithm is just one part of a step counting system, as motion data must be captured from user before the algorithm can act on it
This system must include wearable hardware to allow real-time data capture from a moving user
A step counting system must contain several elements that allow it to both collect data and perform the calculations required to execute the algorithm:
  Sensors
  Wireless communications hardware
  Battery
  CPU

## Slide 13: Systems for “smart” step counting with neural networks
Two systems have been developed as a means to evaluate the use of artificial neural networks as a step counting solution
  1. Raspberry Pi-based system
    Pedometer implemented using Python scripts running on a single-board computer
  2. Custom implementation
    Pedometer implemented by an 8-bit microcontroller-based system
Both are intended to use the same machine learning model for step classification
  System 1 (“Pi solution”) can perform classification on-board or off board
  System 2 (“Custom solution”) requires an external host for classification due to a lack of computing power

## Slide 14: Solution I: Raspberry Pi
Objective of this solution was to evaluate neural networks as a technique for step counting
  Linux OS and ARM processor allow execution of Keras program to perform on-board classification of motion data, so classification may be performed both on and off the board.
Advantages
  Allows use of high-level APIs and programming languages to implement pedometer and connectivity functions to speed up development time
  Complete PCB with external interfaces to hardware accessories
  Linux OS provides a familiar development environment
  No client system required for operation
Disadvantages
  Power-hungry! Pi demands 540 mA when CPU is idle.
  OS and Python libraries are clunky and abstracted, true time-sensitive routines not possible due to pre-emption by system processes
  Cost and complexity: far too much for what is required here!
  Inclusion of extra hardware is clunky, only 40-pin header allows small-footprint expansion

## Slide 15: Solution II: Custom hardware
Objective was to evaluate the use of PCB centered around an 8-bit microcontroller as a solution to issues faced by Raspberry Pi solution
  Low processing power of microcontroller precludes on-board classification; all classification is performed off-board by another host.
Advantages
  Bare-metal implementation allows programmer complete control over microcontroller’s CPU functions and peripherals
    Timers, interrupts, serial hardware
  Considerably lower power consumption
  On-board power solution
Disadvantages
  Client system required for operation
  PCB cannot be purchased COTS and must be developed as a bespoke system
  PIC18 software routines must be developed specifically for this application
  Minimalist implementation means no on-board classification!

## Slide 16: Client system
The client system connects to the pedometer through a wireless connection and is intended to perform motion classification
  Optional for Pi solution, required for custom solution
  Bluetooth Classic for Pi solution, Bluetooth Low Energy for custom solution
Client system features significantly more capable hardware than Pi Broadcom CPU and can perform classification in a shorter amount of time
Client software implementation is different between two solutions, but core functionality is retained
  Implementation changes due to fundamental differences between Bluetooth Classic and Bluetooth Low Energy protocols

## Slide 17: Raspberry Pi solution
Pi runs Python scripts to implement three main functions
  Data polling
    Collect data from Pi Sense Hat’s on-board IMU to characterize motion (10Hz)
  Off-board communication
    Bluetooth Classic link to laptop host to exchange motion data and classification results
  Motion classification
    Runs motion classifier on-board whenever a host is not connected over Bluetooth
Program attempts to take advantage of parallelism to minimize blocking delays from I/O and classification functions
  Pi is a 4-core system: we want to make use of all hardware resources!
  Uses Unix sockets and file I/O for inter-process communication between each component script
  True parallel thread execution difficult due to Python Global Interpreter Lock

## Slide 18: Software used by Raspberry Pi solution
Many Python libraries used for implementation of key components
Keras
  High-level API for TensorFlow functions
  Interface for neural networks in Python
Pybluez
  Library allowing use of Bluetooth Classic functions in Python
    No longer actively supported, but still works on Linux with Python 3.10
  Allows implementation of RFCOMM sockets in Python program
Pi Sense Hat API
  Provides software interfaces to Sense Hat hardware
  RTIMU component of this API used for retrieving data from LSM9DS1 IMU

## Slide 19: How the Pi solution works
Pi solution’s operation can be described by a simple flow chart

## Slide 20: Hardware design considerations
The prototype solution’s Raspberry Pi core introduces challenges to portability due to the high power consumption required and lack of developer control over the hardware due to the operating system
  Bare metal: a device that operates without the overhead of an operating system; program code is run directly by chip
The new solution shall be a bare-metal based solution in order to:
  Allow the developer more control over software implementation
    Processor interrupts, sleep states, timing
  Lower power consumption
    Back to basics: include only essential hardware to save power!
  Improve real-time performance
    No OS overhead, threads, etc.

## Slide 21: In defense of removing on-board classification from custom solution
No need to put hardware for classification on custom solution, everyone already carries a powerful CPU in their pocket!
iOS/Android client application can replace the need for on-board hardware to perform motion classification
  Same functions as client system / program
  Many mobile processors contain dedicated machine learning hardware to accelerate classification
    Example: iPhone neural engine
  Application can make use of Android/iOS ML interfaces
    CoreML for iOS, TensorFlow Lite for Android

## Slide 22: Hardware solution trade study
Several options were considered to implement the hardware solution
Arduino Nano 33 BLE
  Built-in Bluetooth hardware, IMU, and microcontroller
    All-in-one solution, does not require significant hardware development
      But not enough control over AVR processor w/ Arduino bootloader…
      Limited control over interrupts, timers, low-power modes, etc.
ESP32 development boards
  Built-in wireless interfaces and microcontroller
  But power consumption is too high!
    ESP32 cores run at high clock speeds (>80MHz)
Custom implementation
  Design custom circuitry and fabricate own PCB to implement device
  Add on-board power solution to enhance portability
  Selected PIC18 for microcontroller as I am most familiar with that architecture and these devices tend to be cheap and readily available from major distributors
    Powerful on-chip peripherals available (timer, hardware serial ports, external interrupts)
    Core can run at 3.3V and operate at low clock speeds (<20 MHz) to save power

## Slide 23: Hardware design
Microcontroller core: PIC18LF2420 @ 4 MHz
  8-bit microcontroller with RISC instruction set, programmed in C
Power source: 18650 lithium-ion cell, 9V DC adapter
  Uses standard barrel jack for external power / charging
Wireless connectivity: HM-10 Bluetooth Low Energy module
  Complete PCB assembly integrated into design through serial port header
Sensor suite: Raspberry Pi Sense Hat
  Intended for use with Raspberry Pi, but PIC18 microcontroller talks to LED matrix and LSM9DS1 IMU over I2C bus

## Slide 24: Software required for custom solution
Unlike Pi solution, all software on the pedometer itself is packaged in the form of a unified C executable
Once again, Keras is used on the client side to perform motion classification on data polled from the pedometer.
  The client itself, however, has been rewritten to perform BLE GATT writes in lieu of Bluetooth Classic RFCOMM socket communications.
  For simplicity, client is now a CLI program and has no GUI
Bleak library for Python 3.10 used to implement Bluetooth Low Energy communications on the client side
  Replaces the Pybluez library used to implement Bluetooth Classic communications for the Pi solution

## Slide 25: Power and battery solution
System requires a long-lasting battery
  System is designed to be used out and about, so battery life should be a priority
  Old system used 10000mAh power bank, but drained quickly due to power requirements of Raspberry Pi
Solution: Protected 18650 lithium-ion cell
  Lithium-ion cells can be dangerous for use in wearables, but protected cells contain circuitry to mitigate overheating, overcharge, and over-discharge events
  High power density: model used on step counter has capacity of 3500mAh!
On-board charging system consists of a linear battery charging IC implementing CCCV algorithm, relay, DC-DC converter, and 9V DC adapter
  Linear charge controllers are cheap, effective, easy to integrate
  Charge rate: 500mA, or C/6 (6 hours to full charge from 0% state of charge)
  Single-pole, double-throw relay cuts battery from circuit during charging, uses external DC adapter to both charge the battery and run the on-board circuitry

## Slide 26: Power and battery solution (continued)
Although a single lithium-ion cell features a significantly lower capacity than a 10 Ah power bank, battery life is significantly greater in the custom hardware solution than with the Raspberry Pi
  Note: Benchmarks are used to calculate power consumption of Pi, as CPU power consumption is dependent on processing load
Best case performance for Pi: 18.5 hours
  10000 mAh / 1010 mA (benchmark value) = 18.5 hours
    Assumes CPU is at idle, which may be the case with off-board classification
Worst case performance for Pi: 9.9 hours
  10000 mAh / 1010 mA (benchmark value) = 9.9 hours
    Assumes CPU is 100% maxed out, which is often the case with on-board classification
Worst case performance for custom solution: 5.3 days!
  3500 mAh / 27.3 mA (observed value) = 128.2 hours, or 5.3 days
  Nearly 7 times the battery life of Pi solution with off-board classification!

## Slide 27: Battery sense circuit
Normally, dedicated BMS or gas gauge would be used for battery management
  Uses techniques such as Coloumb counting for higher-fidelity charge estimation
  Cost-prohibitive for this application; protected battery allows more risk here.
Simple circuit used to sense battery voltage to approximate state of charge
  Circuit uses resistors and MOSFETs to scale and switch battery voltage into on-chip ADC to save battery
  Microcontroller activates MOSFETs to allow current to flow through voltage divider resistors, then voltage is read through 10-bit ADC
    Saves power by only allowing current to flow through voltage divider whenever a voltage read takes place.
Low current draw of system allows close approximation of battery open-circuit voltage
  Which can be mapped to state of charge!
  Low battery LED triggered when

## Slide 28: PIC18 software architecture
Application program developed in C with Microchip’s XC8 compiler
  C compiled for PIC18 architecture
Uses an interrupt-based program to reduce power consumption
  Microcontroller core sleeps when BLE connection is inactive
    HM-10 module wakes up PIC18 core with external interrupt when a connection is active
  Periodic update of battery voltage reading
    ~1 second timer interrupt
  Data is only collected and sent in response to user requests
    19200 baud serial communications used to communicate with HM-10, serial interrupt triggers a response
Makes use of on-chip hardware for interfaces to peripherals
  UART: HM-10
  I2C: LSM9DS1 (Sense Hat)
  10-bit ADC: Battery level sensing
  GPIO: Digital inputs and outputs for battery sense circuit, HM-10 digital interrupt