## Slide 1: Solar Energy Generator: Design Rendering Description
Prototype system will be mounted in a pelican case with battery and other peripherals.
Laser Cut Delrin Panel will cover all electronics and have display, buttons and a rotary encoder mounted to it.
All front panel electronics will connect to the main PCB via a wiring harness with 0.1” header pin connectors. Future iterations will use JST connectors.
Souriau UTS circular connectors allow sealed external connections to loads and sources.

## Slide 2
Back
Enter
Select
Display
Load
Solar Energy Generator:
Front Panel Diagram
Pelican Case
Delrin Front Panel
OLED Display
Rotary Encoder
Momentary Push Buttons

## Slide 3
Solar Energy Generator:
Internal case layout
Pelican Case
Port A
Port B
Port C
Port D
PCB
5V Buck Module
LiFePO4 Battery
I2C/SPI Isolator

## Slide 4: Port Connections
Souriau UTS 8 Pin connectors
Ports A and B: Solar Panel Input, Battery Voltage output
Ports C and D: Regulated 5V output, Battery Voltage output
All connectors share the same body, but different pin locations are populated depending on function. Connection something to the wrong port wont cause any damage.
Each port Contains locations for Panel+, Panel-, Battery V+, Regulated V+, GND, Control, and pins for future expansion with sensors and digital communication.

## Slide 5
Programming
Buttons
Display
Power Stage
Gate Drive
Voltage + Current Sense
Voltage + Current Sense
MCU
Load switch relays
De bounce
12V, 5V, 3.3V, 1.8V Regulators
Panel Input
SPI, SCI, GPIO
Battery Terminal
Load Output 2
Load Output 1
Battery Temp, I2C
Solar Energy Generator:
Final PCB Overview

## Slide 6
Solar Energy Generator:
A Usage Scenario
Battery
Solar Panel
LED Lamp
Microcontroller, Light sensor, Wireless radio
Serial Interface

## Slide 7
Solar Energy Generator:
Final PCB 3D View