## Slide 1: Capacity for Position
Pierce Nichols
Teardown 2025

## Slide 2: Motivation
Bendy SAO
Robot Sailboat

## Slide 3: What can we buy?
Environmentally Sealed Rotary Position Sensors are Expensive
~$100/sensor for on-axis
  Rotational axis is prime real estate
~$1000/sensor for off-axis
All non-starters for things like Bendy SAO

## Slide 4: What About Capacitance?
Capacitive touch hardware built into most microcontrollers
Sensors are just PCBs, so we can do whatever we want
It should work for linear position as well

## Slide 5: First Try
ESP32 dev board
Adafruit touch library
Four pads in pairs set at 90 degrees (sin and cos)
Stepper mounted for test/evaluation
Doesn’t really work…

## Slide 6: Microchip QTouch
Adafruit Feather M0 board
QTouch library
Two-layer mutual inductance rotor
Stepper mounted for test/evaluation
Defeated by auto-calibration

## Slide 7: Something a little different
Adafruit Feather M0 board
Outer drive ring
Two split inner sense rings, rotated 90 degrees
Drive Sine A
Sine B
Cosine A Cosine B
Rotor (half copper)

## Slide 8: Equivalent Circuit
Internal impedance too low, uncertain

## Slide 9: A better circuit
Near infinite input impedance
Accurate drain resistance

## Slide 10: Revised board
Adafruit Feather M0
A4988 stepper driver
Shielding ground plane on the back

## Slide 11: Sensing procedure
Put a square pulse on the drive ring
Wait for a set period
Measure the voltage on the sense pin
Repeat once for each sense pin

## Slide 12: Calculate the angle
This corrects for small deviation from time & contamination
Result is not quite right, but close enough to linearize

## Slide 13: Results
“Sine” and “Cosine” are triangle waves (sort of)
Raw accuracy is ±10 degrees
With filtering & linearization, can get ±3 degrees
Good enough for Bendy SAO, not for sailing robot

## Slide 14: A different approach
Sinusoidal excitation
Each leg of the circuit functions as a variable high-pass filter.
We can use a lock-in amplifier to filter most of the noise.

## Slide 15: Review of Lock-in Amplifier
Multiplication of two sines
If both frequencies are equal, we get a component at twice the frequency and one at zero frequency
Even the worst low pass filter (like time averaging) will produce a very narrow bandpass filter.

## Slide 16: Quick Check with Saleae & Jupyter

## Slide 17: Sources of Non-Linearity
Capacitive coupling to nearby metal
  Probably not – experiments with adding & subtracting parts didn’t change behavior
The four legs of the circuit influence each other
  Confirmed by disconnecting legs

## Slide 18: Conclusion
Bendy SAO
Robot Sailboat

## Slide 19: Future Work
Experiment with different size rotors
Experiment with different rotor arrangements
Write a library for sinusoidal excitation
Figure out how to deal with calibration for QTouch

## Slide 20: References & Resources
QTouch App Note https://www.mouser.com/pdfDocs/QTouch_QTAN0079.pdf
QTouch Layout Guide https://www.microchip.com/content/dam/mchp/documents/OTH/ApplicationNotes/ApplicationNotes/Atmel-42094-QTouch-Schematic-and-Layout-Checklist_ApplicationNote_AT02259.pdf
Capacitor Impedance Calculator https://www.allaboutcircuits.com/tools/capacitor-impedance-calculator/
Capacitance Calculator https://www.omnicalculator.com/physics/capacitance
Modifying Arduino IDE Serial Plotter https://github.com/arduino/arduino-ide/issues/803#issuecomment-1338149431
Basic Capacitive Position Library https://github.com/logos-electromechanical/CapPosnBasic
Hackaday IO page https://hackaday.io/project/203347-capacity-for-position

## Slide 21: QUESTIONS?
piercenichols@gmail.com
Mastodon: @nocleverhandle@social.seattle.wa.us
BlueSky: @nocleverhandle.bsky.social
And I am currently looking for work